## Slide 1: Designing a 16-Bit RISC-V Processor with 8 Instructions Using Vivado

## Slide 2: Agenda for Today's Presentation
Introduction to the Project
Processor Architecture and Instruction Set
Instruction Implementation
Simulation
Testing
Conclusion and Future Work

## Slide 3: The team
Ilia Panayotov
Esra Mehmedova
Esin Mehmedova
Yiğit İlk
Paul Hagner

## Slide 4: Introduction to the Project

## Slide 5: Project Objectives and Goals
Design a 16-bit Processor
  The project aims to design a functional 16-bit processor capable of executing eight specific instructions, enhancing computational capabilities.
Understanding Digital Design
  We aim to deepen our understanding of digital design principles, which are crucial for successful hardware implementation.

## Slide 6: Introduction to the PYNQ-Z2 Board
FPGA Development Board
  The PYNQ-Z2 board serves as an FPGA development platform, enabling advanced hardware designs and digital signal processing projects.
Xilinx Zynq-7000 SoC
  This board is based on the Xilinx Zynq-7000 System on Chip, integrating programmable logic with an ARM processor for versatile applications.
Custom Processor Design
  The combination of programmable logic and ARM processing capabilities allows for custom processor designs tailored to specific applications.

## Slide 7: Processor Architecture and Instruction Set

## Slide 8: Overview of the 16-Bit Processor Architecture
Register File
  Stores temporary data and instructions for quick processor access.
  Arithmetic Logic Unit (ALU)
  Performs arithmetic operations for instruction execution.
  Processor
  Directs data flow and manages instruction execution.
  Data Memory
  Stores and retrieves data needed during execution.
  Instruction Memory
  Holds program instructions for the processor to execute.

## Slide 10: Instruction Set
  Custom 16-bit RISC-V instruction set, that includes arithmetic, branching, memory, and immediate value operations

## Slide 11: Instruction Implementation

## Slide 12: ADD/ADDI/SUBI instructions
Purpose
  ADD: reg_a + reg_b = result
  ADDI: reg_a + imm = result
  SUBI: reg_a – imm = result
Signed Integer Values
  Understanding signed integers is crucial, as they can represent both positive and negative values in calculations.
Notes: The ADD command performs addition on two signed integer values, contained in two registers. The SUBI and ADDI are operations that add/subtract value from the register and a value contained in the instruction.
All of the operands are signed, so they include both positive and negative numbers.

## Slide 13: BEQ & JARL
  Purpose
  Modify the program counter (PC) to alter control flow, enabling conditional or unconditional jumps.
Conditional Branching (BEQ)
Compare reg_a to reg_b
If they are the same: next_pc = pc + imm
If they are different: next_pc = pc + 1
Jump and Link Register (JARL)
  Store pc in reg_a
  ‎next_pc = reg_b

## Slide 14: LUI: Load Upper Immediate
Purpose
  Manipulate computer registers by setting upper bits to facilitate calculations.
  ‎Takes a 10-bit immediate value(imm) and shifts it left by 6 bits.
  The lower 6 bits are filled with zeros(6’b0).
  The result is store in reg_a
  This helps in storing large numbers or addresses efficiently.

## Slide 15: LW & SW
Purpose
The instructions are used to read from and write to memory.
LW: Load Word (Half)
  Loads a value from memory into a register.
  The memory address is calculated using a base register and an offset.
  SW: Store Word (Half)
  Stores a register’s value into memory.
  The memory address is calculated the same way as in LW.

## Slide 16: How do we fetch instructions?
Using the PC, we output the respective instruction.
Each instruction is building on the results of the previous operations.

## Slide 17: Simulation

## Slide 18: Scheme for the Simulation Environment in Vivado

## Slide 19: Dual port AXI Instruction memory
The approach to:
Handle Write Addresses for addressing where in memory of the slave to write to
Hanle Write Data of the data being put into the slave memory.
The approach to:
Initialize the Verilog processor file

## Slide 20: Dual port AXI Instruction memory
We had to bypass the given axi template memory file, which fetches new instructions in the processor. And replace it with instructions fetched by us manually.

## Slide 21: Dual port AXI Instruction memory
At the end we had to make sure that the result we got from the processor was correct format:
In addition, we needed to provide the output to the Python implementation that was executing the processor:

## Slide 22: Testing and Validating the Processor on Hardware
Before testing the operations on the hardware we need to generate the bit file.
To create the bit file we are using Vivado.
After creation of the file we get such notification in Vivado and we are ready to test.

## Slide 23: Testing

## Slide 24: Using Waveforms and integrated programme counter for tests
Testing if it all actually works
  We can simply just create iverilog signal waveforms to actually test if everything is working thanks to our programme counter, but if we want to take it to the next level, we need actual access to the FPGA running our bit file.

## Slide 25
Using Waveforms and integrated programme counter for tests
  Here on the left, you can see our integrated testing with the programme counter actually working with all of the functions.

## Slide 26: Using Python and Pynq library to conduct real life tests
  Here, we have the mmio class integrated into our PYNQ Z2 board's Python interface.

## Slide 27: Using Python and Pynq library to conduct real life tests
  Here, we have the mmio class integrated into our PYNQ Z2 board's Python interface.

## Slide 28: Using Python and Pynq library to conduct real life tests
  The Overlay IP we created for our setup with the AXI can be communicated through the Python code allowing us to read portions of the memory.
  But unfortunately it only allows us to read and write only 2*32 bits.

## Slide 29: Conclusion and Future Work

## Slide 30: Challenges Faced and Solutions Implemented
Encountered Challenges
  The project faced several challenges, including bugs in the code and issues with integration.
Debugging Techniques
  We implemented various debugging techniques to identify and resolve coding issues effectively and efficiently. Testing various inputs of 16-bit numbers and comparing them to the output

## Slide 31: Potential Improvements and Future Work
Enhancing Processor Design
  Future improvements can focus on enhancing processor design by implementing a simpler processor file and creating a control unit.
Making it fully function on the Pinq board
  Optimizing the code for input of the instructions and output, so it is functioning with the Verilog we created for the brains of the project.
Exploring New Features
  Exploring additional features like interrupts and advanced memory management can significantly enhance processor capabilities.